National Spherical Torus Experiment

NSTX

SYSTEM REQUIREMENTS DOCUMENT

DIAGNOSTICS

NSTX-SRD-4X-016

Revision 1

June 16, 2010

________________________________

Robert Kaita

WBS DIAGNOSTICS Manager

________________________________

Lawrence Dudek

NSTX Project Engineering Manager

________________________________

Masayuki Ono

NSTX Project Manager

| Revision | Date | TRB | Description of Change |
| --- | --- | --- | --- |
| 0 | 7/23/97 |  | First Issue |
| 1 | 6/16/10 |  | Update to reflect status of diagnostics at completion of NSTX-Upgrade (NSTX-U) |

Introduction	4

DIAGNOSTIC System Requirements	8

1.0 Functions	8

1.1 Baseline Diagnostics	8

1.1.1 Plasma Control	8

1.1.2 Confinement and Transport	8

1.1.3 MHD Stability	8

1.1.4 Scrapeoff Layer and Divertor Physics	9

1.2 Upgrade Diagnostics	9

2.0 Configuration Requirements and Essential Features	9

2.1 Diagnostic Port Requirements	9

2.2 Requirements for Internal Diagnostics	10

2.3 Diagnostic Vacuum System Requirements	11

2.4 Electrical Power and Isolation Requirements	11

1

List of Tables

D-1	baseline nstx diagnostics summary	5

D-2.1-1	nstx diagnostic port requirements	9

APPENDICES

A.1 LIST OF REFERENCES	12

# Introduction

The purpose of plasma diagnostics is to provide information on discharge parameters to characterize NSTX plasmas and guide NSTX operations for optimized performance. Those diagnostics that will be available when operations resume after the completion of NSTX-Upgrade (NSTX-U) are called baseline diagnostics. They are listed in Table D-1 with the designation “unaffected” or “available on day 1 after upgrade” in the column labeled “status after upgrade.”

Nearly all of the baseline diagnostics were installed and operational prior to NSTX-U. They either do not need any changes, or require minimal modification, as a result of the upgrade. The major exceptions are the center stack diagnostics and the multi-spatial point, multi-time point Thomson scattering (MPTS) system for electron temperature and density profiles. New magnetics, Langmuir probes, and thermocouples shall be installed on the new center stack. The MPTS system shall be redesigned to so that the larger diameter of the center stack does not interfere with its laser trajectories.

The NSTX-U program continues the NSTX emphasis on detailed measurements of plasma profiles for understanding the basic confinement and transport properties of 5 second, radio frequency-driven NSTX discharges with auxiliary heating. Some diagnostics are not included in the baseline set because of the cost and complexity of redesigning and relocating them after the installation of the new center stack and the second neutral beamline. They are listed in Table D-1 with the designation “eliminated” or “available within first year after upgrade” in the column labeled “status after upgrade.” Issues related to these diagnostics are summarized in the comments that follow Table D-1.

The long-term objective continues to be to upgrade and expand the diagnostic set further for the study of fluctuations and transport in long pulse, neutral beam-heated NSTX plasmas. In addition, plasma diagnostics shall provide input for advanced plasma control systems. New concepts and systems developed by the national NSTX team to implement these goals also shall be encouraged.

| Table D-1: Diagnostics Summary [R1, R2] |
| --- |
| Diagnostic | Affected by CSU? | Affected by 2nd NB? | Status following upgrade |
| Magnetics for equilibrium reconstruction1 | Y | N | available on day 1 after upgrade |
| Diamagnetic flux measurement2 | Y | N | available on day 1 after upgrade |
| Multi-pulse Thomson scattering (MPTS) (30 ch, 60 Hz)3 | Y | N | available on day 1 after upgrade |
| Charge-Exchange Recombination Spectroscopy (CHERS): Ti(R) and V(r) (51 ch)4 | N | Y | available on day 1 after upgrade |
| Poloidal CHERS (P-CHERS): V(r) (75 ch) | N | N | unaffected |
| Beam Emission Spectroscopy (BES) (32 ch) | N | N | unaffected |
| Neutral particle analyzer (2D scanning)5 | N | Y | eliminated-displaced by 2nd NB; replacement available within first year after upgrade |
| Far-infrared tangential interferometer polarimeter (FIReTIP) (119m, 6 ch)6 | N | Y | eliminated-displaced by 2nd NB |
| Interferometry/forward scattering (1 mm, 1ch) | N | N | unaffected |
| Visible bremsstrahlung detector (1 ch) | N | N | unaffected |
| Midplane tangential bolometer array | N | N | unaffected |
| X-ray crystal spectrometer: Ti(0), Te(0) (Bay L)7 | N | Y | eliminated-displaced by 2nd NB |
| Motional Stark Effect – Collisionally-Induced Fluorescence (MSE-CIF) (18ch) | N | N | unaffected |
| Motional Stark Effect – Laser-Induced Fluorescence (MSE-LIF)8 | N | Y | available on day 1 after upgrade |
| High-n and high-frequency Mirnov arrays | N | N | unaffected |
| Ultra-soft x-ray arrays – tomography | N | N | unaffected |
| "Optical" soft x-ray array | N | N | unaffected |
| Fast X-ray tangential camera (2s)9 | N | Y | eliminated-displaced by 2nd NB |
| Microwave reflectometers (65 Ghz backscattering, correlation, FM/CW, fixed frquency)10 | N | Y | available within first year after upgrade |
| Tangential microwave scattering (high-k)11 | N | Y | eliminated-displaced by 2nd NB |
| Fast lost-ion probe (energy/pitch angle resolving)12 | N | Y | available on day 1 after upgrade |
| Neutron detectors (2 uranium and 4 fast scintillator) | N | N | unaffected |
| Locked-mode detectors13 | N | Y | available on day 1 after upgrade |
| RWM sensors (n = 1, 2, and 3)14 | N | Y | available on day 1 after upgrade |
| Gas-puff Imaging (2sec)- midplane and divertor | N | N | unaffected |
| Langmuir probes-PFC tiles15 | Y | N | available on day 1 after upgrade |
| Edge Rotation Diagnostics (Ti, V, Vpol) | N | N | unaffected |
| 1-D CCD H cameras (divertor, midplane) | N | N | unaffected |
| 2-D divertor fast visible camera | N | N | unaffected |
| Divertor bolometer (20 ch)16 | N | N | unaffected |
| IR cameras (30Hz) (3) | N | N | unaffected |
| Tile temperature thermocouple array17 | Y | N | available on day 1 after upgrade |
| Scrape-off layer reflectometer | N | N | unaffected |
| Edge neutral pressure gauges | N | N | unaffected |
| Fast visible camera | N | N | unaffected |
| Visible survey spectrometer | N | N | unaffected |
| UV survey spectrometer (SPRED)18 | N | Y | available within first year after upgrade |
| VUV transmission grating spectrometer19 | N | Y | available within first year after upgrade |
| Fission chamber neutron measurement | N | N | unaffected |
| Visible filterscopes | N | N | unaffected |
| Wall coupon analysis | N | N | unaffected |
| Vertical x-ray crystal spectrometer (Bay D) | N | N | unaffected |
| LLNL EUV spectrometer XEUS (Bay L)20 | N | Y | available on day 1 after upgrade |
| LLNL EUV spectrometer LoWEUS (Bay E) | N | N | unaffected |
| Fast camera view of RF antennas (Bay L)21 | N | Y | available within first year after upgrade |
| Sample probe | N | N | unaffected |
| Fast ion D diagnostic | N | N | unaffected |
| Biased Electrode and Probe (BEAP) | N | N | unaffected |
| Edge deposition monitors | N | N | unaffected |
| Edge Neutral Density Diagnostic (ENDD) | N | N | unaffected |
| Langmuir probe array-inter-LLD | N | N | unaffected |
| Langmuir probes-RF antenna | N | N | unaffected |
| Langmuir probes-outboard edge | N | N | unaffected |
| RF edge magnetic probe | N | N | unaffected |
| Plasma TV | N | N | unaffected |
| SWIFT 2-D flow diagnostic | N | N | unaffected |

Comments:

1. Replace/enhance equilibrium magnetics on center stack.

2. Install new diagmagnetic loop through centerstack or continue to use TF as diamagnetic loop.

3. MPTS upgrade to accommodate new CS: relocate beam dump, re-aim laser, re-aim viewing optics (may require Bay F port cover modification), and modify viewing optics.

4. No good location for CHERS background view with 2nd NBI. Present plan is to re-install background view at Bay L and rely on beam notching. Other possibilities being investigated.

5. Eliminate existing scanning NPA with 2nd NBI. Replace with array of fixed SSNPAs.

6. Eliminate FIReTIP with 2nd NBI. Relocation would be difficult.

7. Eliminate x-ray crystal spectrometer (Bay L) with 2nd NBI.

8. Edge MSE-LIF sightlines blocked by extension of beam armor toward Bay G for 2nd NBI. Modify armor and add graphite insert to DNB hole in armor. Incorporate these features into 2nd NB design.

9. Eliminate fast tangential SXR camera with 2nd NBI.

10. Microwave reflectometers are at Bay J which will move out. In-vessel horns may need to be moved closer to plasma.

11. Eliminate present tangential microwave scattering (high-k) diagnmostic with 2nd NBI. Relocation of existing system not possible. Investigate implementation of new system with k capability at different location.

12. Needs to be modified to accommodate expanded vacuum vessel at Bay J.

13. Locked-mode detectors need to be relocated inside vessel for 2nd NBI.

14. RWM sensors need to be relocated inside vessel for 2nd NBI.

15. Fixed Langmuir probes on center stack need to be replaced.

16. Bay J midplane array needs to be modified to accommodate expansion of vacuum vessel.

17. Tile temperature thermocouple array on center stack needs to be replaced.

18. UV survey spectrometer (SPRED) to be relocated from end of pumping duct to new Bay L port cover.

19. EUV transmission grating spectrometer needs to be relocated.

20. LLNL EUV spectrometer (XEUS) (Bay L) to be relocated from end of pumping duct to new Bay L port cover.

21. Fast camera view of RF antennas (Bay L) to be relocated to new Bay L port cover.

# Diagnostic System Requirements

## 1.0 Functions

### 1.1 Baseline Diagnostics

The function of baseline diagnostics shall be to support basic machine operations. They shall also support the near-term emphasis of the NSTX program. This shall be effected by detailed measurements of plasma profiles for understanding the basic confinement and transport properties of 5 second, radio frequency-driven NSTX discharges.

The baseline diagnostics are listed in Table D-1.[R1] They shall support the NSTX program in the following areas.

1.1.1 Plasma Control and Equilibrium

For discharge position, shape, and current determination, there shall be flux loops, Rogowski loops, pickup coils, and visible TV cameras.

1.1.2 Confinement and Transport

a. For electron temperature and density profile measurements, the baseline diagnostic set shall include the MPTS system.

b. For ion temperature measurements, there shall be a charge-exchange spectroscopy system (CHERS) for ion temperature profile measurements. The spatial resolution shall be ≈5 cm (using the TFTR heating beam) and the time resolution shall be ≈30 ms. There shall be a high-throughput CHERS background array that also serves as visible continuum diagnostic for Zeff profile measurements.

c. For impurity measurements, there shall be a vacuum ultraviolet survey spectrometer (SPRED) with a spectral resolution of ≈2Å over 100Å-1200Å, and a time resolution of 1 ms. There shall also be a visible spectrometer with a spectral resolution of ≈1Å over 2000Å-7500Å, and a time resolution in the range of 50-100 ms. There shall also be high-resolution “short wavelength” and “long wavelength” extreme ultraviolet spectrometers (XEUS and LoWEUS) for detailed impurity identification.

d. For current profile measurements, motional Stark effect polarimetry based on collisionally-induced fluorescence (MSE-CIF) using the first neutral beamline shall continue to be used. Laser-induced fluorescence MSE (MSE-LIF) using a dedicated diagnostic neutral beam shall also be available after NSTX-U operations resume.

1.1.3 MHD Stability

a. Magnetic pickup coil arrays shall be used to provide external mode information.

b. Vertical and horizontal soft X-ray diode arrays shall be used for soft X-ray profile measurements with 2-3 cm spatial resolution and 0.001 ms temporal resolution.

1.1.4 Scrapeoff Layer and Divertor Physics

a. Diagnostics in the plasma facing components shall include Langmuir probes and thermocouples for edge plasma measurements.

b. Visible and IR cameras, bolometers, H detectors, and a visible spectrometer shall be used as spectroscopic and bolometric diagnostics for edge plasma measurements.

### 1.2 Upgrade Diagnostics [R2]

The most significant profile diagnostics that are not included in the baseline set are the far infrared tangential interferometer polarimeter (FIReTIP) for line-averaged density measurements, and the tangential microwave scattering (high-k) turbulence diagnostic.  It could be possible to reinstall them in the future, but the cost and complexity of redesigning and relocating them after the installation of the second neutral beamline may make this difficult. They are thus listed in Table D-1 as “eliminated” in the column labeled “status after upgrade.”

## 2.0 Configuration Requirements and Essential Features

### 2.1 Diagnostic Port Requirements

a. After the completion of NSTX-U, the plasma diagnostics on NSTX shall continue to connect to the vacuum vessel and support structure (WBS 12) at the machine interface vacuum valve and/or the points of mechanical support for the diagnostic inside the vacuum vessel. The largest impact on diagnostics of the changes necessary for NSTX-U is on midplane access. The following large midplane ports shall be available primarily for diagnostics. The major diagnostics utilizing these ports are given in Table D-2.1-1. Diagnostics shall continue to use space on the large midplane ports in Bay H and I.

| Table D-2.1-1: NSTX Diagnostic Port Requirements |
| --- |
| Location | Diagnostic System |
| Large midplane port - Bay B | CHERS and MSE-CIF |
| Large midplane port - Bay F | MPTS |
| Large midplane port - Bay G | Ultrasoft X-ray arrays, single-channel interferometer, tangential bolometer, and MSE-LIF |
| Large midplane port - Bay J | Microwave reflectometry |
| Large midplane port - Bay L (replaces large midplane port at Bay K that is used for second neutral beamline) | Visible spectrometer Survey spectrometer (SPRED) EUV spectrometer |

b. All diagnostics connected to NSTX shall be compatible with a 150o C bakeout temperature at the torus isolation valve.

2.2 Requirements for Internal Diagnostics

a. All coils, loops, and other diagnostics mounted inside the vacuum vessel shall be compatible with a 350o C bakeout temperature for the plasma facing components and a 150o C bakeout temperature at the flanges which provide the interfaces to the diagnostics [R3].

b. All coils, loops, and other diagnostics mounted inside the vacuum vessel shall be installed in a way that minimizes damage due to interaction with the plasma. This includes protection against high voltages and large heat loads, particularly for components located on the center column.

c. The number of coils and loops shall be as follows.

A) Center Stack:

• 15 flux loops

• 2 plasma current Rogowski loops

B) Inner Vacuum Vessel:

• 13 B() and B() coils

• 12 "2-D" [B() and B()] coils

• 6 internal flux loops

• 6 halo Rogowski loops

C) Outer Vacuum Vessel:

• 19 "2-D" [B() and B()] coils

• 18 internal flux loops

• Additional high-frequency Mirnov coil arrays

#### d. Thermocouples shall be placed on the backing plates of the plasma facing tiles in the main plasma chamber (including the passive stabilizer plates) and the divertor region.

e. All materials utilized within the primary vacuum boundary shall be on the PPPL Vacuum Committee approved list, or shall be approved by the committee [R4].

2.3 Diagnostic Vacuum System Requirements

a. The vacuum system, if required, for each diagnostic shall be included in the diagnostic fabrication task. This includes, for example, forepumps, turbopumps, cryopumps, and associated controllers.

b. The exhaust outlets for forepumps shall be provided as part of the NSTX vacuum pumping system (WBS 31).

2.4 Electrical Power and Isolation Requirements

a. All diagnostics shall be isolated via optical and/or magnetic (isolation transformer) means prior to exiting the test cell boundary. The isolation shall be rated to withstand a one minute AC hipot test at 20 kV AC rms [R5].

b. All ancillary components which are in mechanical contact with the vacuum vessel shall be electrically isolated from the vacuum vessel. The isolation shall be rated to withstand a one minute AC hipot test at 2 kV AC rms [R5].

c. Diagnostic elements which must be located in the center stack between the OH coil ground plane and the center stack casing (e. g., Rogowski coils and flux loops) shall be referenced to ground and shall be insulated to withstand the full coaxial helicity injection (CHI) voltage. The insulation shall be rated for a one minute  DC hipot test at 5 kV [R6].

d. All connections to and from diagnostic equipment in the NSTX test cell shall be with optical fiber. All connections between the data acquisition systems for each diagnostic shall be with optical fiber.

e. AC power for diagnostic signal processing, data acquisition, and control subsystems shall be derived from the general 480V AC distribution system at D-site. However, sufficient isolation and/or filtering shall be provided to ensure that the quality of the input power (flicker, noise, harmonics) applied to the diagnostic systems is adequate for their reliable operation.

f. Each diagnostic shall be independently grounded to a single point ground as determined by the NSTX machine grounding specifications.

g. Diagnostic components located outside of the NSTX Test Cell shall be electrically isolated to permit safe access while NSTX is operating.

A.1 List of References

| R | Description | Value | Units | Reference |
| --- | --- | --- | --- | --- |
| 1 | Baseline Diagnostics Set | na | na | GRD Table 1.5.1 |
| 2 | Upgrade Diagnostics | na | na | GRD sec 1.1.2.b |
| 3 | Bakeout Requirements | na | na | GRD sec 2.3.2 |
| 4 | Vacuum Material Requirements | na | na | GRD sec 1.1.4.c |
| 5 | Electrical Isolation Requirements | na | na | GRD sec 1.1.5 |
| 6 | Center Stack Electrical Isolation Requirements | na | na | GRD sec 1.5.b |