## Slide 1: Inboard Diverter Tile Concepts Comparison
Design
  Baseline with crossing T-Bars
  Single Larger T-Bar
  Single Larger T-Bar Split and Pinned (ala TFTR)
  Three Point Rotating Supports
  Smaller Tiles – 7.5 vs 15 deg – with Single Larger T-Bar
  Smaller Tiles – 7.5 vs 15 deg – with Single Larger T-Bar – GRAFOIL under Base with 10 kN Preload on T-bar
All concepts subjected to the following:
  Thermal - 5 MW/m2 for 5 sec
  Eddy Currents – Br_dot= 520 T/s, Bz_dot=460 T/s for 1 ms
  Halo Currents – 35 kA per 15 deg Tile
Results driven by Tensile Stress at Supports in ATJ

## Slide 2
Ibdhs102810/Ibdhs001_struct
Baseline

## Slide 3
Ibdhs112410/Ibdhs009_structx
Larger T-Bar

## Slide 4
Ibdhs011011/Ibdhs804_struct
Split and Pinned
T-Bar

## Slide 5
Ibdhs010511/Ibdhs703_struct
Three point pivoting supports

## Slide 6: Pivoting Supports Details
Not to scale
Bolt
T-Bar
Spherical Washers
Retaining Clips

## Slide 7
Ibdhs120810/Ibdhs101_struct
Ibdhs120810/Ibdhs101_struct19
Smaller 7.5deg Tile

## Slide 8
Ibdhs120810/Ibdhs101_struct21
Smaller 7.5deg Tile
Grafoil under base of Tile and T-bar
T-bar Preloaded to 10 kN
Preload only much lower

## Slide 9: Summary
Design Concept | Peak Principal Tensile Stress, MPa, Th+EM | Peak Principal Tensile Stress, MPa, Th Only
Baseline with crossing T-Bars | 85.8 | 
Single* Larger T-Bar | 56.2 | 19.4
Single Larger T-Bar Split and Pinned (ala TFTR) | 57.7 | 
Three Point Pivoting Supports | 32.4 | 7.44
Smaller Tiles – 7.5 vs 15 deg – with Single Larger T-Bar | 37.7 | 14.1
Smaller Tiles – 7.5 vs 15 deg – with Single Larger T-Bar – GRAFOIL under Base with 10 kN Preload on T-bar | 30.8 | 23.6
*Single T-Bar Concepts need to provide radial constraint not explicitly modeled

## Slide 10: Conclusions
Baseline with crossing T-Bars
  T-slot to small to carry launching force and over turning moments from EM loads. Over constrains tile from thermal load
  Single Larger T-Bar
  Show improvement over baseline (above) but still over constrains tile from thermal along T-bar axis
Single Larger T-Bar Split and Pinned (ala TFTR)
  Attempt to relieve thermal stress along axis – While flexible for thermal, unable to distribute launching load
Three Point Rotating Supports
  Allows fairly free thermal expansion. Stress dominated by EM launching forces
Smaller Tiles – 7.5 vs 15 deg – with Single Larger T-Bar
  Significant reduction compared to larger tile with Single Larger T-Bar
  Gain in thermal stress for smaller tile less than expected due Tile/Tbar relative stiffness
Smaller Tiles – 7.5 vs 15 deg – with Single Larger T-Bar – GRAFOIL under Base with 10 kN Preload on T-bar
  Reduces impact of EM loads (ie behaves like preloaded joint) but increases constraint from thermal load

## Slide 11: Conclusions
Recommend design that shows better performance for thermal loads, while still performing adequately with EM loads
  Thermal loads are more predictable. Better thermal margin may allow for higher heat fluxes if EM loads prove to be less severe
  EM loads are less certain and analysis has assumed the worse