## Slide 1
NSTX
Supported by
College W&M
Colorado Sch Mines
Columbia U
CompX
General Atomics
INEL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Nova Photonics
New York U
Old Dominion U
ORNL
PPPL
PSI
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Washington
U Wisconsin
NSTX Upgrade Project
NB Peer Review
LSB, B318
April 19, 2011
Neutral Beam Upgrade: NB Armor
Culham Sci Ctr
U St. Andrews
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Hebrew U
Ioffe Inst
RRC Kurchatov Inst
TRINITI
KBSI
KAIST
POSTECH
ASIPP
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
U Quebec
K. Tresemer, M. Denault, J. Winkelman, L. Bryant

## Slide 2: NB Armor: Overview
Armor Relocation:
  Shifting armor counterclockwise
    To fit both beamlines on surface
  Using ATJ graphite in non-crucial areas of armor.
    Carbon Fiber Composite (CFC) in areas of intense beam overlap
  Upgrading mounting hardware to maximize port functionality and installation/removal
    Look at disruption forces and resulting stresses on armor mounts

## Slide 3: Armor Move
Current Alignment
Proposed Alignment
BL 2
BL 1
BL 1
Bay I
Bay H
Bay I
Bay H
Bay G

## Slide 4: Armor Move: Beamline fit
Used combination of empirical data and analysis to create beam “footprints”
  Beam photo shows rough ellipse shape from conditioning shots
  Assumed beam dispersion of .5 deg horizontal, 1.5 deg vertical
  Used calculated “Smear” areas for beam profiles (incident angle effects)
  Taking these areas, built ellipses and applied them to a simple armor shape, showing beam layout and overlaps
C
B
A

## Slide 5: Armor Move: Beamline fit
Outer ring:
20% total source power
Inner “hotspot”:
80% total source power
Resulting Source Profiles on Armor Face Confirms Fit!
Beam overlaps create areas of intense flux
Area of thermal investigation and probable material upgrade to 3D CFC

## Slide 6: Armor Tile Thermal Analysis
Model accuracy check
  Data from MSE shots
    ATJ tiles
    90 kv, 19 MW/m^2 source heat flux, 400 ms
    50 – 80 C bulk temp change
      Confirmed that ALGOR model behaved similarly
1 NB “fault” testing
    Temperature and Stress under full power, full length of shot
        80 kV, 7.7 MW/m2, 5 sec
        90 kV, 9.2 MW/m2, 3 sec
        110 kV, 13.9 MW/m2, 1 sec
    Baseline Material properties of ATJ Graphite
      Max Tensile Stress: 26 Mpa
      Max Temp : 2600 °C*
      *This is the temperature at which the sublimation rate rapidly accelerates. Sublimation does begin at lower temperatures in vacuum, but the effect is less. Attempting to capture an acceptable maximum temperature.

## Slide 7: Armor Tile Thermal Analysis
 | Run # | Run Description | T (deg C) | Time @ T (s) | Tslot Von Mises (MPa) Free exp.
1 Beamline | 1 | MSE, 90 kV, .400 ms, 9.24 MW/m^2 applied |  |  | 
 | 2 | Stress analysis | 544.6 | 0.433 | 8.91
 | 3 | 80 kV, 5 s, 7.70 MW/m^2 applied |  |  | 
 | 4 | Stress analysis | 1893.7 | 5.5 | 16.16
 | 5 | 90 kV, 3 s, 9.23 MW/m^2 applied |  |  | 
 | 6 | Stress analysis | 1611.3 | 3.08 | 16.76
 | 7 | 110 kV, 1 s, 13.86 MW/m^2 applied |  |  | 
 | 8 | Stress analysis | 1220.3 | 1.05 | 16.42
 | 9 | Stress analysis | 956.4 | 1.2 | 17.78

## Slide 8: Armor Tile Thermal Analysis
2 NB “fault” testing
    Temperature and Stress under full power of two beams
      Looking at an overlap tile that sees greatest flux
      Finding time limit to max temp and max stress
        80, 90, 110 kV
 | Run # | Run Description | T (deg C) | Time @ T (s) | Tslot Von Mises (MPa) Free exp.
2 Beamlines | 11 | 80 kV, max q: 23.9 MW?m^2 |  |  | 
 | 12 | Stress analysis, TS 14 | 2693.9 | 1.68 | 36.6
 | 13 | Stress analysis, TS 8 | 1965.2 | 0.96 | 25.6
 | 14 | 90 kV, max q: 35.8 MW/m^2 |  |  | 
 | 16 | Stress analysis, TS 18 | 2643.3 | 1.08 | 37.88
 | 15 | Stress analysis, TS 10 | 1905.54 | 0.6 | 26.1
 | 17 | 110 kV, max q: 35.84 MW/m^2 |  |  | 
 | 18 | Stress analysis, TS 18 | 2649.4 | 0.675 | 38.68
 | 19 | Stress analysis, TS 10 | 1879.7 | 0.375 | 26.86

## Slide 9: Armor Tile Thermal Analysis
Results
  Single NBL “fault” is acceptable
    Temperatures and stresses within capabilities of ATJ graphite
    Possible surface cracks, ablation
      If occurs, should attempt to visually inspect surface for damage
  Double NBL “fault” is not acceptable with only ATJ
    Stresses on surface and in T-slot exceed material limit
      Risk critically cracking tile. Need to prevent this.
        Use available CFC in needed zones. Tensile strength 3x that of ATJ.
      Temperatures will surpass 2600 °C and carbon will rapidly sublimate.
        Material mass will be sufficient to protect for length of “fault”. Stainless backing plates added protection.
        Armor will be damaged, need visual inspection, but will perform duty as a sacrificial protective surface.
      Increased safety:
        Additional Plasma interlock
        Increasing ss backing plate coverage
        Increased administrative caution while using both NLBs

## Slide 10: Thermal Analysis for Between-Shot Cooling
Worst case heat load on tile and backing plate
  Ran test sample in ALGOR, simple shape
    “Back of the envelope” Analysis
    3”x1” slice of armor (tile and backing plate), 3/8” cooling tube, 20 minutes between shots
    Determined time constant for cooling: ~70 seconds
  Preliminary results suggest cooling system adequate for in-between shot cooling
      More tests needed to confirm. Numbers will be updated for FDR as analyses are completed

## Slide 11: Thermal Analysis for Between-Shot Cooling
Graphite (ATJ)
Stainless Steel

## Slide 12: Armor Support System
Weld on studded pads (4 places)
Bay I footprint
Front
Bay G footprint
MSE LIF Port

## Slide 13: Armor Support System
Redesigned Bay H supports
Bay G support
Back
Bay I support

## Slide 14
The Solid Model is Symmetric about 2 planes
Only ¼ of Armor model will be included in the FE analysis
Neutral Beam Armor Solid Model

## Slide 15: Transient Dynamic Von Mises Stress (Outboard Displacement Disruption)
Max Stress = 1.6e7 Pa = 2,320 psi
Vessel Interface
Weld Interface
Bolt Stress
Flange 2
Flange 1
Vessel Edge 1
Vessel Edge 2
Plate Support
The Transient Equivalent Stress at Max Current is less than 10 Ksi
and well within the material strength capacity (Based on Merged Solids)

## Slide 16: Thermal Growth
Addressed potential thermal growth issues with the new armor constraints
  Used bake-out temps as an example
  Shows that SS plates grow “up and out”
  Do not cause tile interference

## Slide 17: Thermal Growth
Addressed potential thermal growth issues with the new armor constraints
  Used bake-out temps as an example
  Shows that SS plates grow “up and out”
  Do not cause tile interference
Direction of Thermal Growth

## Slide 18: Conclusions
Armor Relocation: Thermal
  6 sources fit adequately upon armor face
  In areas of high heat flux (source overlaps), tile material will be replaced with 4D CFC
      CFC has multi-plane high k, thermal shock resistance, good mechanical properties
  Armor will sufficiently protect the VV from NB exposure, even with increased heat flux from source overlap
  Cooling lines will be adequate for heat removal between shots
Armor Relocation: Mechanical
  New mounting scheme improvement to accessibility
      Employing bay H and G as access points
  Disruption analyses show that forces in the mounts are low, material and fasteners are adequate for loading
      Consider final analysis with updated load scenarios and non-merged model
  Thermal growth in plates will not cause issues with tiles
  Installation procedure is being created
  Armor drawings are complete (barring any other changes to design).