From: "Timothy N. Stevenson" <tstevens@pppl.gov>

Date: March 12, 2009 11:38:51 AM EDT

To: "Alfred von Halle" <avonhalle@pppl.gov>

Cc: "Mike Williams" <williams@pppl.gov>, "Erik D. Perry" <eperry@pppl.gov>, "Mark B. Cropper" <mcropper@pppl.gov>, "John W. Edwards" <JEdwards@pppl.gov>

Subject: NBI Upgrade Weekly Status 3/13/09

Al,

NBI Decon:  The first pumpout of the BL has been completed. The stack monitor did not indicate any discernible Tritium level. Several air vents and pumpouts will be performed followed by an internal sample and smear measurement to quantify results. Cabling and tray removals have started. Cables will be decontaminated and saved for reuse. The BL Lid stand material is being collected in the shop and fabrication is starting.

NBI Power and Control:  Lists of cables have been developed and are under review. Focus has been on the bending magnet system to evaluate whether reuse of some of the existing cable length is feasible. Cable routing design through buildings will start when a designer is assigned.

NBI Duct: Modeling of BL and aiming angles has begun using the existing duct as a reference. External BL features including platforms will also be included in the general arrangement drawings.

NBI BL Services: Several different cryogenic piping routes and techniques are being evaluated for heat loads and maintenance requirements. A walkdown of existing cryogenics piping was performed where possible by the two Cog Engineers on this job. This effort will continue next week during the NSTX maintenance week when NTC access is available.

NBI Management: Effort continues to properly staff the CDR Engineering requirements, especially pertaining to the Armor design work. An electrical designer is scheduled to start at the end of this month to support Power systems.

Regards,

Tim

Timothy N. Stevenson

Head of Experimental Heating Systems & Neutral Beam Operations

LSB 316  C Site

Princeton Plasma Physics Laboratory

Princeton University

P.O. Box 451

Princeton, NJ 08543

Office (609) 243-2657

FAX (609) 243-3248

email: tstevenson@pppl.gov

Skypager # : 2047351